## Slide 1: Introduction to CHROMOSOME Architecture, core concepts and core component
CHROMOSOME Workshop, Spitzingsee, 15.06.2011
Simon Barner, Christian Buckl, Michael Geisinger, Gerd Kainz, Nadine Keddis, Dominik Sojer, Stephan Sommer, Hauke Stähle
fortiss GmbH
An-Institut der Technischen Universität München

## Slide 2: Terminology
CHROMOSOME (actually without the “H”…)
Cross-Domain: automation, multimedia, automotive, etc.
Modular: consists of software components with “plug & play”
Operating System: provides hardware abstraction
or Middleware: provides communication infrastructure
XME = CHROMOSOME
Abbreviation required for prefixes (e.g., functions in the code)
X: represents “Cross-domain” in the literal sense
ME: represents “Middleware” or “Modular Middleware”

## Slide 3: Introduction
XME provides…
Platform abstraction (PAL)  Operating System features
Communication infrastructure  Middleware features
Node management
Firmware generation
Multi-platform support
Notes: Topic = Name + Definition (~ Semantics)

## Slide 4: XME Architecture (1)
Application and Quality of Service Model
Service and Platform Repository
Generated Application
Generated Middleware
Operating System
Hardware Abstraction Layer (HAL)
Model Transformation and Code Generation
≈
Target Platform
Target Platform
…

## Slide 5
Anwen- dungs- und Dienstgüte-modell
Dienste- und Plattform-bibliothek
Generierte Anwendung
Generierte Middleware
Betriebssystem
Hardware-Abstraktionsschicht (HAL)
Modelltransformation und Codegenerierung
≈
Zielplattform
Zielplattform
…

## Slide 6: XME Architecture (2)
function calls
data centric communication
XME
Project
Platform Abstraction Layer (OS + HAL) (hal)
Primitive (prim)
Advanced (adv)
Core (core)
Primitive (prim)
Advanced (adv)
Generated Middleware
Generated Application
Generated PAL
Notes: HAL aufteilen in projektspezifische und XME-übergreifende Komponenten
Für eine HW-Funktionalität kann es mehrere Primitive geben, wobei nur ein Primitiv pro Middleware-Instanz ausgewählt werden darf
Mode Switch: Falls benötigt: über Aktivierung/Deaktivierung von Funktionskomponenten

## Slide 7: Core Concepts: Data Centric Communication
Node 2
Node 3
Node 1
Data Centric Communication (DCC)
Topic = Assign semantics to data based on an ontology (e.g., Temperature)
Publication = Intent to make data of a certain topic available
Subscription = Request to receive data of a certain topic
Sensor 1
publish( Temperature )
Sensor 2
publish( Temperature )
Display
subscribe( Temperature )
IP over Ethernet
Serial
data centric communication

## Slide 8: Core Concepts: Data Centric Communication
Knoten 2
Knoten 3
Knoten 1
Data Centric Communication (DCC)
Topic = Assign semantics to data based on an ontology (e.g., Temperature)
Publication = Intent to make data of a certain topic available
Subscription = Request to receive data of a certain topic
Sensor 1
publish( Temperature )
Sensor 2
publish( Temperature )
Anzeige
subscribe( Temperature )
IP über Ethernet
Seriell
datenzentrische Kommunkation

## Slide 9: Core Concepts: Meta Data (1)
data centric communication
Meta Data
Meta data = Set of keys and associated values
  Describe data of a specific topic in more detail
  Examples: data type, location, timestamp, accuracy
Publications are annotated with meta data
Subscriptions can filter by meta data
Sensor 1
publish( Temperature | location = “Dijkstra”, unit = “°C” )
Display
subscribe( Temperature | location = “Dijkstra”  unit = “°C” )
Sensor 2
publish( Temperature | location = “Ada”, unit = “°C” )

## Slide 10: Core Concepts: Meta Data (1)
datenzentrische Kommunkation
Meta Data
Meta data = Set of keys and associated values
  Describe data of a specific topic in more detail
  Examples: data type, location, timestamp, accuracy
Publications are annotated with meta data
Subscriptions can filter by meta data
Sensor 1
publish( Temperature | location = “Raum 1”, unit = “°C” )
Anzeige
subscribe( Temperature | location = “Raum 1”  unit = “°C” )
Sensor 2
publish( Temperature | location = “Raum 2”, unit = “°C” )

## Slide 11: Core Concepts: Meta Data (2)
Static Meta Data
Meta data that are statically assigned to topics
  Examples: data type, accuracy, unit, (location)
Dynamic Meta Data
Meta data that are dynamically attached to data
  Examples: (location), confidence
Quadrocopter Sensor Driver
publish( Temperature | location = ?, accuracy = 0.1, unit = “°C” )
Display Driver
subscribe( Temperature | location = “Dijkstra”  unit = “°C” )
Sensor Driver 1
publish( Temperature | location = “Dijkstra”, unit = “°C “)
Dynamic
runtime
filtering
?

## Slide 12: Core Concepts: Request/Response
Request/Response Communication (RR)
Client/server based communication scheme
Efficient routing of request and response
Node 1
data centric communication
Client
request( ?Address , !Address )
Node 2
Broker routes request to server and response back to client
Node 3
Server
handleRequest( ?Address , !Address)
Broker
Broker
Broker

## Slide 13: Optional Core Components
Mode Switch (MS)
Dynamic activation and deactivation of software components during runtime

## Slide 14: Core Components (1)
Platform Abstraction Layer (PAL)
Application Component
Scheduler
Network Interface
GPIO
ADC
…
Routing Table
data centric communication
XME
Middle-ware
Appli- cation
XME
PAL
Direc- tory
Broker
Node Manager
PAL components
Mandatory XME core components
Advanced components
Optional XME core components
Login Server

## Slide 15: Core Components (1)
Hardware-Abstraktionsschicht (HAL)
Anwendungsspezifische Komponente
Netzwerk-schnittstelle
GPIO
ADC
Routing- Tabelle
datenzentrische Kommunkation
XME
Middle-ware
Appli- cation
XME
PAL
Ressourcen-verwaltung
Broker
Knoten- verwaltung
PAL components
Mandatory XME core components
Advanced components
Optional XME core components

## Slide 16: Kernkomponenten (1)
Hardware-Abstraktionsschicht mit Betriebssystem
(z.B. FreeRTOS + lwIP + STM32 SPL auf STM32F10xxx)
Datenbank-Anbindung
Netzwerk-schnittstelle
GPIO
ADC
Routing- Tabelle
Middle- ware
Anwen- dung
Treiber
Ressourcen-verwaltung
Broker
Knoten- verwaltung
Messwert-Erfassung
Plausibilitäts-prüfung
Vorver- arbeitung
datenzentrische Kommunkation
Netzwerkanbindung (z.B. Ethernet)

## Slide 17: XME Core Components
Application
Execution Manager
…
Routing Table
data centric communication
Login Server
Node Manager
Directory
Resource Manager
Platform Abstraction Layer (PAL)
Ethernet Periphery
Communication Library
GPIO Periphery
ADC Periphery
Operating System / Board Support Package
Inter-rupts
Communication Negotiator
PAL components
Mandatory XME core components
Advanced components
Optional XME core components
Hardware periphery
Broker
Interface Manager
TCP Plug-in
UDP Plug-in
ADC Arbiter
GPIO Arbiter
ADC
GPIO

## Slide 18: XME Core Components
Primitive Components
Advanced Components
Execution Manager
Routing Table
Login Server
Directory
Resource Manager
Hardware Abstraction Layer (HAL)
Ethernet Periphery
Communication Library
GPIO, ADC, … Periphery
Operating System / Board Support Package
Interrupts
HAL components
Mandatory XME core components
Advanced components
Optional XME core components
Hardware periphery
Broker
Interface Manager
TCP Plug-in
UDP Plug-in
Node Manager
…
Function call
Data centric communication
GPIO, ADC, … Drivers
Resource Abstraction
Primitive components

## Slide 19: Core Components (2)
Routing Table
  Stores all routing entries (local and remote) for all paths passing this node
Broker
  Responsible for accessing and providing data in Chromosome
  Represents central component of Chromosome
Dictionary
  Database handling publications and subscriptions. Communication paths are calculated and established by the Dictionary.
Node Manager
  Responsible for system start up. Stores central information of node (configuration data, node id, …)
  Takes care of login procedure

## Slide 20: Core Components (3)
Scheduler
  Manages execution order of tasks. Task can be registered by all components on demand.
Login Server
  Assigns node ids and other information (node id hosting dictionary, …) to new nodes in the network
Network Driver
  Takes care of sending and receiving data over a specific network interface
  Address resolution (node id -> physical network address) is done here
Platform Abstraction Layer (PAL)
  Abstracts from concrete platform (platform = HW + OS + Middleware)
  Offers standardized interface to access platform components
  Division between PAL and XME components is blurred

## Slide 21: Current Status
Existing Concepts
Design of core components
Design of primary life cycle use cases (e.g., login, data transmission)
Preliminary implementation of IP-based network communication on Windows/POSIX
Partial HAL implementation for some embedded target platforms (ARM)
Existing Infrastructure
Redmine
Working CMake-based build system (tested on Windows)
Preliminary source code documentation

## Slide 22: Contact
  Michael Geisinger
  fortiss GmbH – An-Institut der Technischen Universität München
  Guerickestr. 25 | 80805 München | Germany
  Tel. +49 89 289 – 18111 | Fax +49 89 289 – 18107
  geisinger@fortiss.org | www.fortiss.org